## Slide 1: Direct Electron-Beam Injection Experiments for Validation of Air-Chemistry Models
S.B. Swanekamp, J.R. Angus, D. Mosher*, P.F. Ottinger*, A.S. Richardson, and J.W. Schumer
Plasma Physics Division, Naval Research Laboratory, Washington DC 20375
*Independent contractor to NRL through Engility Corp., Alexandria, VA 22314
Presented at the EuroAsian Pulsed-Power Conference
Estoril, Portugal
Sept. 17-23, 2016

## Slide 2: There are 3-facilities at NRL where air-chemistry is currently being studied
A low-voltage arrangement to study SGEMP
  Febetron is used to generate 100 kV, 5 kA, 90 ns pulses
  Interaction volume on the order of 101010 cm3
A higher voltage arrangement in a large “space” chamber to study SREMP
  Febetron is configured to provide a 200 kV, 10 kA, 90 ns pulse
  Interaction volume on the order of 200200200 cm3
Gamble II is used to generate a 1 MeV, 800 kA, 50 ns beam for material response studies
  Interaction volume on the order of 101010 cm3
~10 kA/cm2
<< 1 kA/cm2

## Slide 3: The low-voltage arrangement is used to validate SGEMP

## Slide 4: A large 2-m diameter “space” chamber to simulate SREMP
200-kV beam into space chamber for SREMP

## Slide 5: Ring diode experiments on the Gamble II produce 800-kA, 1-MeV ebeams with Jb>10 kA/cm2
Transport Diagnostics
An axial pinhole camera (PHC) images x-rays from the anode plane and endplate
B-dot sensors inside the gas cell measure net current
Laser interferometry measures line-integrated electron density along a diameter
Time-resolved spectroscopy measures lines from various species
anode foil
diagnostic
spool
ring
cathode
0.1-10 Torr N2
I/2
I/2
Gamble II
(-) center
conductor
A-K gap
e-
e-
Gamble II
door
insulator
Gamble II Ring Diode
Ring Diode Electrical Characteristics
10-cm radius
beam
7-cm radius
beam
Jb exceeds 10 kA/cm2 at the entrance to the gas cell
High current density supported by x-ray images
shot 8141
shot 10765

## Slide 6: Gases with pressures of 1-10 Torr provide charge and current neutralization for intense propagating ebeams
Both charge neutralization (ne > nb) and current neutralization (In = Ib - Ip <IA) are needed to transport beams with currents exceeding the Alfvén current IA = 17 bg kA over distances much larger than the beam radius.
Beam-impact ionization breaks down the initially-neutral gas, creating a conducting plasma
The plasma electrons gain energy from the inductive electric field produced by the time-varying net-current In , causing further ionization through thermal processes.
Applications
  Intense electron-beam transport for material-response studies
  Gas-discharge studies
  E-beam propagation in air
  Systems-response studies
  Radiography
Nitrogen is the natural gas to use in the ABC model

## Slide 7: A new gas-chemistry model is needed for these high-current density beams
Weakly ionized model [1,2]
  ne-n>>ne-e so that eedf determined by the inelastic energy-loss collisions (ne<0.01 ngas)
  Chemistry is relatively simple because electrons always interact with neutral gas in the ground state
    Ground state N2
      e+N2  e+N2*
      e+N2  e+N2+
    NO Stepwise ionization
      e+N2*  e+N2+
    NO Dissociative recombination
      e+N2+  2N
    NO additional chemistry for atomic nitrogen needed
  Momentum transfer occurs through elastic collisions with neutral gas
1) D. McArthur and J. Poukey, PRL, 27, 26 (1971), and Phys. Fluids, 16, 11 (1973)
2) D. Welch, et al., Phys. Plasmas 1 (1994)
3) J. Angus, et al., Modeling nitrogen plasmas produced by intense electron beams, Physics of Plasmas, 23, 053510 (2016)
Advanced breakdown and conductivity (ABC) [3]
  ne-n<<ne-e so that eedf is Maxwellian (ne<0.01 ngas)
  Chemistry is more complex and electrons can interact with excited ground state as well as reaction products
    Ground state N2
      e+N2  e+N2*
      e+N2  e+N2+
    Stepwise ionization
      e+N2*  e+N2+
    Dissociative recombination
      e+N2+  2N
    Additional chemistry for atomic nitrogen needed
  Momentum transfer occurs through electron-ion collisions rather than electron-neutral collisions

## Slide 8: The ABC model contains 42 different nitrogen species to include the important kinetic processes
Energies for molecular excitations and Z = 1 atomic-species excitations are with respect to the molecular ground state
Excitation (ionization) energies of atomic species with Z > 1 are with respect to the Z = 1 ground state
Species set is sufficiently inclusive to
  Describe the transition from weakly-ionized and molecular to strongly-ionized and atomic
  Determine the role of step-wise processes to ionization and dissociation
  Predict the production rate characteristic line radiation from N2, N2+, and N species
swarm

## Slide 9: Thermal electron reaction rate constants are computed using energy-dependent cross sections
Y. Itikawa, J. Phys. Chem. Ref. Data, Vol. 35 (2006)
P. Teulet, et al., J. Quant. Spect. & Rad. Trans. 62 (1999)
A.V. Kosarim, Chem. Phys. Lett. 414 (2005)
J. Peterson, J. Chem. Phys. 108 (1998)
Y. Wang et al., Phys. Rev. A 89 (2014)
R. Henry et al., Phys. Rev. 178 (1969)
Y. Kim and J. Desclaux, Phys. Rev. A 66 (2002)
W. Lotz, Z. Physik 216 (1968)
Molecular Reactions
Atomic Reactions
5,6
7,8
1
1,2
1,3
1
4
Rate Constants

## Slide 10: Beam-impact reactions are described using the stopping-power formalism1,2
Energy needed to produce an electron-ion pair W, and production efficiencies η for molecular and atomic nitrogen are given by Slinker, Taylor, and Ali 1,2
Beam-impact contributions to the rate equations for each species are from
This formalism accounts for both direct beam-impact ionization and ionization produced by intermediate energy (~ 60 eV) secondary electrons as they relax to thermal energies
W and η are basically constant for electrons with energies of 1 keV to 1 MeV
Bethe stopping power in 1-Torr nitrogen for energies between 0.1 and 1 MeV is between 6.4 and 2.8 eV/cm
R. Taylor, et al., J. Appl. Phys., Vol. 64, no. 3, pp. 982-993, (1988).
S. Slinker, et al., J. Appl. Phys., Vol. 67, no. 2, pp. 679-690, (1990).
Beam-impact reactions do not perturb the beam in a 10-cm-long transport cell

## Slide 11: The parameter regime of the GII experiments permit the use of simplifying assumptions in nitrogen plasma modeling
Pressure is high enough that plasma electron collisions are local (small mean free path)
The ionization state is sufficiently high early in the pulse so that
  background electrons are approximately Maxwellian (ne-e > ne-n > 1/tb)
  rate equations are dominated by electron-impact reactions (can ignore heavy-heavy reactions and photon-induced reactions)
The plasma is stationary on the hydrodynamic time scale of JpB and ambipolar diffusion
Thermal energies during the molecular phase are high enough so that ionization, dissociation, and electronic excitation dominate over vibrational and rotational excitations
Parameter Regime of GII experiments

## Slide 12: Time-dependent plasma behavior in ABC was tested with a 0D circuit model and rigid-beam approximation
Good charge and current neutralization in many GII experiments allow the beam to travel ballistically through the gas cell
Assume the ring beam travels rigidly in z between radii r1 and r2 in a cell with conducting walls at rw
Assume Jb and Jp = σpEz are axially invariant and uniform between r1 and r2 with area Ab
The beam-plasma system is modeled as an simple L-R circuit with a time-dependent conductivity σp(t) driven by a time-dependent beam current Jb(t)
The ABC model is used to compute the plasma conductivity σp(t)
OD rigid beam model

## Slide 13: The ABC model extends nitrogen gas chemistry to high electron-beam current densities
Weakly
Ionized
ABC
Coronal regime
-

## Slide 14: The plasma current history from simulation is in good agreement with that from experiment
Plasma current is nearly equal to beam current since the current neutralization factor is small (fn=In/Ib<<1)
Experimental and simulated net current agree within about a factor-of-two
Net current measurements and modeling have possible errors due to
  experimental: low measured currents in a difficult plasma environment
  OD ABC modeling: rigid paraxial beam can’t respond to net-current B field and will not have correct injected angular distribution
Plasma current is the important parameter for background plasma modeling since Joule heating is the main power source
Net current is important for beam pinching

## Slide 15: The net current is ‘frozen in’ at a small fraction of the beam current early in the pulse
Simulation parameters
  Inner and outer beam radii r1=6.5 cm and r2=7.5 cm
  gas cell radius rw=10 cm
  p=1-Torr N2
Conductivity rises over the entire beam pulse
Beam current about 95% neutralized by the plasma return current
Inet = Ib - Ip

## Slide 16: neL from simulation is in good agreement with experimental neL measurements
Experimental neL measured across beam diameter with a two-color interferometer2 (green at λ = 532 nm and IR at 1064 nm)
Phase shift proportional to density
Phase shift transitions from molecular ions to atomic ions over the beam pulse
Plasma ions are mostly atomic during the last 100 ns
Comparison of Simulated and Experimental Line Densities

## Slide 17: The gas transitions from weakly-ionized molecular to strongly-ionized atomic over the current pulse
Molecular nitrogen density is mostly gone by the end of the pulse
The gas is mostly atomic during the latter half of the pulse
Electron momentum-exchange is dominated by collisions with neutrals during the first 50 ns, then by collisions with ions for the rest of the pulse
-3]

## Slide 18: Electron temperature is determined by a balance of Joule heating PJ and inelastic losses
Beam heating Pb is negligible in comparison with Joule heating
The energy sink is dominated by inelastic collisions with ground and metastable states
  molecular ground state N2(X1) early in pulse
  neutral atoms N(4S,2D,2P) near peak current
  atomic ions N+(3P,1D,1S) near end of pulse
Te spikes early in the pulse due to the large inductive electric field of the un-neutralized beam
During the weakly-ionized phase Te = Te(E/P)
Reduced electric field remains below the runaway value of about 1.25kV/cm/Torr
Energy Balance
Temperature History

## Slide 19: Ionization and dissociation are dominated by processes with high-lying excited-energy states
Ionization potential of ground state atomic N is 14.5eV
Numerous optically-allowed states of neutral atomic nitrogen have energies between 10.4 eV and 13 eV
Dissociation potential of N2(X1Σ) is 9.75 eV
Dissociation to atomic species initially goes through the ground state N2(X1Σ), but proceeds mostly through N2+ and excited N2(*) states as their populations grow
total
total

## Slide 20: The OD ABC simulations reproduce experimental scaling trends of ne and fn=Inet/Ib with pressure
Both ne and fn show modest increase with pressure in range 0.5 to 10 Torr
0D results using new gas-chemistry model are in much better agreement with old experiments than a previous 2D LSP model1 using
  PIC beam particles
  a weakly-ionized gas-chemistry model
  dissociative recombination turned off
For these data, Inet from the ABC model is lower than the experiment by a factor of 2-3 for pressures near 1 Torr
1) S. Strasburg, et al., Phys. Plasmas 10, 9 (2003).

## Slide 21: Agreement between simulated and experimental Inet is improved on some recent shots on GII
shot 10765, P = 1 Torr
shot 10766, P = 5 Torr
Similar diode voltage and current profiles with a 10-cm radius ring diode
Redesigned B-dot monitors may have helped to improve agreement
May need to model the diode and anode foil to get correct beam angular distribution injected into gas cell
2D hybrid simulation in LSP with the ABC can model the self-consistent response of the beam to the evolving electromagnetic fields

## Slide 22: 2D hybrid simulation with LSP shows good transport in 1-Torr nitrogen over 10 cm
ABC model for background plasma
PIC for beam particles
  10 particles/dr/dt
  dr = dz = 1 mm
  Explicit in time (Cm = 0.9)
0.5-mil Ti foil at entrance
Same parameters as considered in 0D simulation
  Diode voltage and current profiles for beam energy and current injected at z=0
  Δrb = 1cm, rb = 7cm
Jb [kA/cm2]
Vb
Ib

## Slide 23
Results at r = 7 cm, z = 1.3 cm
Results at t = 80 ns
Background plasmas at 1 Torr from 2D LSP simulations agree with the 0D modeling

## Slide 24: Electric field and net current from 2D LSP simulations agree with the 0D modeling
Results at r = 7 cm, z = 1.3 cm
Results at t = 80 ns

## Slide 25: 2D LSP hybrid simulation shows poor transport in 10-Torr nitrogen over 10 cm
Vb
Ib
Other than pressure, same simulation as 1-Torr case
Transported beam shows pinching and hose-like instability
Explained by insufficient current neutralization due to lower temperature and conductivity1
Jb [kA/cm2]
R.B. Miller, “Introduction to the Physics of Intense Charged
Particle Beams,” Plenum Press, New York (1985).

## Slide 26: X-ray targets measuring beam propagation and spreading are compared to LSP/ABC simulations
4, 1.3-cm wide,
0.5-mil Ta strips
at z = 3, 6, 9, and 12 cm
X-ray sources in pinhole image
  4-mil Ti anode
  Ta strips,
  0.64-cm poly witness plate at z = 25 cm
  Use lineout between Ta strips to unfold x-ray intensity from Ti anode
pinhole camera photo
shot 10899
z = 12 cm
z = 3 cm

## Slide 27: LSP/ABC simulations show good agreement with transported-beam x-ray measurements
Use I(t), V(t) from shot 10899
Inject beam onto Ti at r = 10 cm, Dr = 1 cm, normal incidence
Calculate Jb(r,z,t) in 1 Torr N2 using:
  ABC model in LSP (effects of scattering, gas chemistry, return currents, fields, etc.)
  Ballistic assumption (scattering in anode followed by ballistic projection to strip locations)
Compare time-integrated Jb(r,z) with x-ray lineouts from Ta strips with ABC and Ballistic models scaled by the same factor
Transport is nearly ballistic, demonstrating good charge and current neutralization
Best agreement with ABC, where residual net current provides slight pinching to fit experiment
Comparison of Pinhole Image Lineouts with Time-Integrated Jb from Modeling
Beam developed azimuthal asymmetries at large z that made comparison more difficult

## Slide 28: Conclusions
The ABC gas chemistry model was developed to describe nitrogen plasmas in the 1-10 Torr pressure range produced by 100-ns REBs with current densities in the 10-kA/cm2 regime
Unlike models in which the gas remains weakly-ionized and molecular, this regime is characterized by nearly complete current neutralization and Joule heating driving the plasma to dissociation and high ionization
The ABC model contains 42 different nitrogen species to properly model the important kinetic processes for this plasma
ABC was coupled to a 0D circuit model that
  provided good agreement with some time histories of neL and net-current measurements
  reproduced scaling of neL and net-current fraction with pressure
2D LSP hybrid-simulations incorporating the ABC model added self-consistent beam dynamics, electromagnetic fields, and scattering, and
  agreed with OD model electron density and net current
  demonstrated excellent agreement with ring beam transport experiments at 1 Torr
  Predicted poor transport at 10 Torr due to insufficient current neutralization

## Slide 29: Future studies are designed to give LSP/ABC a more comprehensive predictive capability over a wider range beam and gas parameters
Perform a new experimental shot series dedicated to benchmarking the gas-chemistry model with time-resolved spectroscopy1
In LSP, couple beam transport simulations to a diode model for more realistic beam injection conditions
  radial current-density distribution
  radial injection-angle distribution entering the anode foil
Investigate nitrogen gas transport at pressures in the 0.1-Torr range to assess the roles of
  nonlocal effects
  large Ωt
  anomalous resistivity due to two-stream instabilities
  electron runaway
Couple a new time-dependent Boltzmann solver to the ABC system of rate equations to properly model low-current-density phenomena for system-response studies
1) J. Angus, et al., to be published in Physics of Plasmas, #POP48751