## Slide 1: Novel Combustion Concepts for Emerging Propulsion Systems: Heated Air Cycle Engines - Extending Mission Range/Endurance Propulsion and Power for days, months, years September 2018
Advanced Concepts Group
Turbine Engine Division
Aerospace Systems Directorate
For Official Use Only

## Slide 2: BLUF
Other countries (Russia and every Nuclear power besides the US, including China, Iran, Pakistan, India, UK, France, and Canada) can develop propulsion and power systems that operate far beyond the capabilities of conventional Hydro-Carbon fuels (ie, 1,000 to 100,000 times the energy density of jet fuels). Von Karman’s 1946 report to Gen Hap Arnold described exactly how to do so and Russia has been using those systems (see 4 month loitering cruise missile).
We (AFRL, DoE, NASA) believe we can develop such a capability and make it potentially safer than conventional fuels. The Heated Air Cycle Engine approach essentially stores energy in a very high density and useful form, enabling ground power, aircraft that don’t require refueling for months, high power/small APU’s, and long range hypersonic vehicles. Imagine the resource savings if we could eliminate 99% of UAS takeoffs/landings, remote airfields and bases, and the need to logistically support jet fuel to field global air power capability.
Imagine the shift in global power if some other country follows von Karman’s 1946 recommendations for the future of Air Power…
If you believe the world won’t be flying on oil in the next century, then who is going to develop that capability?

## Slide 3: Turbine Cycle Energy Input
Combustor
(only used for takeoff/climb/dash)
Heat Exchanger
(sized for cruise power)
Combustor
Conventional Turbine
Heated Air Cycle
Engine (HACE)
Consumes Heat
Waste Heat?
Hybrid Fuel-Cell?
Beamed Power?
Fission?
Fusion?
Positrons?
Isotope Decay
LENR???…
Inherently Simple (only rotating parts)
Waste Heat Leaves as thrust
Throttleable
Consumes Fuel
HACE acts like a self-sustaining recuperated cycle
10

## Slide 4: Ram/Scram Cycle Energy Input
Combustor
(only used for accel/climb/dash)
Heat Exchanger
(sized for cruise power)
Heated Air Cycle
Engine (HACE)
Consumes Heat
Waste Heat?
Hybrid Fuel-Cell?
Beamed Power?
Fission?
Fusion?
Positrons?
Isotope Decay
LENR???…
Throttleable
Consumes Fuel
10
Conventional

## Slide 5: Three ways for high speed HACE (enabling RAM/SCRAM)
RTO-EN-AVT-116
Ram (don’t we care about Isp when ‘fuel’ energy density is 1,000 to 100,000 times conventional)
Supersonic Heat Exchanger
Heated Particle Injection (enables thermal management) or pitch/catch secondary HEX loop (TRL commensurate with illustration)

## Slide 6: Energy Storage
Energy Source Energy density
HC (+ 15 parts air) ~4.3 x 10E6 J/kg
Metals (Al, Boron, etc. + air) ~2-6 x 10E6
H2 (+ 30 parts air) ~12 x 10E6
Methane (CH4) ~5 x 10E6
Explosives ~5 x 10E5
Fuel Cell ~1-5 x 10E5
Battery ~1-3 x 10E4
Spring ~1 x 10E2
Flywheel ~.2-3 x 10E5
Pressure (LN2) ~3 x 10E4
Pressure (3000psi air) ~.4-1 x 10E4
Hydraulic Accumulator ~1 x 10E4
RadioIsotope x 10E9 to 10E11
Fission (U235) ~8.2 x 10E12
25MW portable Fission x 10E1 per second (on semi trailer)
Fusion (D+T) ~5.6 x 10E13
Antimatter (p+e) ~9.0 x 10E15
5
Notes: Portable Fission, 4x10e5 per hour, 2 days ~ 16 MJ/kg (HC at 30% eff), 259 MJ/kg per month, 3x10e9 per year, 3x10e10 per decade…

## Slide 7: Is Nuclear Propulsion and Power Viable?
Viable: Feasible enough to be useful for practical applications:
Long endurance (days to months, longer than conventional systems)
High power density (kW to MW power for conventional tactical/strategic aircraft)
Intrinsically safe (no worse than jet fuel and if we scattered the system across the earth, we wouldn’t have to condemn the area for years)
A few examples which don’t meet these criteria:
6
Notes: Tory II-C, Nuclear Ramjet: Several tests were conducted, culminating in a full-power test on May 20, 1964 where the reactor achieved a steady-state power output of 461 MW and an internal fuel temperature of 1690 K for approximately three minutes.

## Slide 8: Russian Statement on Nuclear Propulsion
"A nuclear-powered underwater drone is something the U.S. knew the Russians were working on... could carry a multi-megaton nuclear bomb with a range of about 10,000 kilometres moving at 56 knots, or 104 km/h and travel to a depth of more than 1,000 metres... capable of carrying a 100-megaton nuclear warhead, which Putin said could target coastal targets and warships.“
"one weapon did surprise some experts: the nuclear-powered cruise missile. 'The nuclear-powered cruise missile is the craziest part,' Geist said. 'Everybody's jaws dropped when that was mentioned because we had no idea they were working on it.' This missile can take an arbitrary path to its target and circumvent any enemy defenses. And the advantage to being nuclear-powered is that it can fly around for months..."
Underwater Drone
4 day endurance
100MT warhead
Faster than conventional torpedoes
Cruise Missile
Months endurance/ loiter
Arbitrary path
Currently possible with fission and hazardous radio-isotope systems (both very effective dirty bombs) as described by the 1946 von Karman report to Hap Arnold
Can we do this with an intrinsically safe system?
Vol 7, Aircraft Fuels and Propellants
7

## Slide 9
Nuclear Energy Summary
Must be Intrinsically Safe in order to relax current VP (or higher) level approval authority to fly.
Fission, Fusion, and Anti-matter not ready for approval any time soon.
Conventional Isotope Decay utilized for very long mission (years), low power density Thermal Electric Generators (RTG) with safety issues.
  RTG Issues:
- Heavy
- Low Efficiency (5% typ)
- Must Reject Waste Heat
Are there isotopes and cycles that could be made intrinsically safe?
Isotope Decay
Process available Exergy
Fission U-235 75 TJ/kg
U-238 (via Pu-239) 77 TJ/kg
Seawater (3.3ppb U) 260 kJ/kg
Th-232 (via U-233) 78 TJ/kg
Fusion H-3 (via Li-6) 269 TJ/kg
H-3 (via Li-7) 162 TJ/kg
H-2 345 TJ/kg
Seawater (156 ppm H-2) 93 MJ/kg
Combustion Jet Fuel 40 MJ/kg
8

## Slide 10: Earth’s Core Heating

## Slide 11: Atomic Transformation Processes
(paper, skin, cell walls)
(aluminum or metal sheet)
(Lead or massive amounts of concrete, earth, …)
(water, concrete)
Alpha (Helium)
Beta – (electron)
Beta + (positron)
Gamma
Neutron
Shielding
Notes: In the human body, Potassium 40 (naturally occurring) 4400 decays per second produce 4000 natural positrons per day (511 keV gamma rays).
Potassium-40 is a rare example of an isotope that undergoes both types of beta decay. About 89.28% of the time, it decays to calcium-40 (40Ca) with emission of a beta particle (β−, an electron) with a maximum energy of 1.33 MeV and an antineutrino. About 10.72% of the time it decays to argon-40 (40Ar) by electron capture, with the emission of a 1.460 MeV gamma ray[1] and a neutrino. The radioactive decay of this particular isotope explains the large abundance of argon (nearly 1%) in the earth's atmosphere, as well as its abundance compared to 36Ar. Very rarely (0.001% of the time) it will decay to 40Ar by emitting a positron (β+) and a neutrino.

## Slide 12: RadioIsotopes (and some key parameters)
Want:
Short half-life (Decay quickly to harmless levels if dispersed?)
Low Radiation (Alpha/Low-energy Beta Decay doesn’t penetrate skin)
High Power per weight (kW/lb)
High Temperature Stability (high melting temperature/low CTE, or stable oxide)
Isotopes: 50,000-4,000,000 x 106 J/kg
Jet Fuel: 40 x 106 J/kg
More data? Other isotopes, secondary/tertiary decay, heat transfer considerations, cost,
derived from Langham, NPS 2013
Notes: 'safe' 2017 leak, only made in Eastern reactors, decays to Rh106 (Rhodium) then quick B- to stable Pd106 (Palladium)

## Slide 13: Energy Storage
Energy Source Energy density
HC (+ 15 parts air) ~4.3 x 10E6 J/kg
Metals (Al, Boron, etc. + air) ~2-6 x 10E6
H2 (+ 30 parts air) ~12 x 10E6
Methane (CH4) ~5 x 10E6
Explosives ~5 x 10E5
Fuel Cell ~1-5 x 10E5
Battery ~1-3 x 10E4
Spring ~1 x 10E2
Flywheel ~.2-3 x 10E5
Pressure (LN2) ~3 x 10E4
Pressure (3000psi air) ~.4-1 x 10E4
Hydraulic Accumulator ~1 x 10E4
RadioIsotope x 10E9 to 10E11
Fission (U235) ~8.2 x 10E12
25MW portable Fission x 10E1 per second (on semi trailer)
Fusion (D+T) ~5.6 x 10E13
Antimatter (p+e) ~9.0 x 10E15
5
Notes: Portable Fission, 4x10e5 per hour, 2 days ~ 16 MJ/kg (HC at 30% eff), 259 MJ/kg per month, 3x10e9 per year, 3x10e10 per decade…

## Slide 14: Radioisotope Decay Air Cycles MQ-1B Case Study
Takeoff/Climbout 100kW
Cruise on 40kW
Internal Combustion Engine
200 lbs
~30% efficient
1080 hr rated life
50 hr maintenance cycles
360 hr overhaul cycle
250 hr MTBF
Fuel: 10 gph for 1 hr
4 gph for 24hrs
Total Fuel ~600 lb
Propulsion and Fuel
~800 lb for 24hrs
Takeoff/Climbout 100kW
Cruise on 40kW
Hybrid Jet Fuel/Isotope Turbine engine
50 lbs
~20% efficient (doesn’t matter much)
20,000 hr life
Fuel: 9 gph for 1 hr
Total Fuel ~100 lb (2x margin)
400kW Isotope Heat Exchanger at mission start, 200kW at half-life.
~30 lbs of Ru 106 (12 months)
64 lbs of Tm 170 (4 months)
Plus HEX Weight
Propulsion and Fuel
200-300 lbs for 3-12 months
(would probably make electric hybrid and double weight)
(Engines are to scale)
12

## Slide 15: Radioisotope Decay Air Cycles MQ-1B Case Study
Takeoff/Climbout 100kW
Cruise on 40kW
Internal Combustion Engine
In 4 months:
12,000 gallons of fuel
($180k at port plus convoy/tanker to point-of issue)
60+ takeoffs/landings
6 engine rebuilds
3 engines
12+ turbochargers
240 sparkplugs
10+ engine ‘failures’
Basing to sustain the above
Takeoff/Climbout 100kW
Cruise on 40kW
Hybrid Jet Fuel/Isotope Turbine engine
In 4 Months:
64 lbs of Tm 170
($192k in Tm 169)
1 takeoff/landing
Flexible Basing/Range
(Engines are to scale)
12

## Slide 16: Beyond Case Study?
Short-Life RadioIsotope Hybrid Turbine Cycles could enable months of mission endurance for a wide variety of platforms
Huge impact upon enormous fuel logistics requirements
Greatly reduces #1 cause of Class A Mishaps (takeoffs/landings)

## Slide 17: Mach 5+?
Consider Alternative Isotopes:

## Slide 18: Potential Demo Systems?
Similar to cruise missile thrust requirements (1000lb payload)
‘Safe’
‘Dirty’
‘Catch up’
Thorium 228 with 1.91yr half-life decays to Stable Pb208 via Alpha/Beta(-) daughters at up to 8 MeV (not low energy), would require shielding (or remote operation) and liquid metal capable HEX

## Slide 19: Summary/ Recommended Path Forward
Nuclear power can enable unprecedented propulsion and power capability for a variety of applications (completely transforming current basing/logistic needs)
US is perhaps the least equipped to take advantage of nuclear power (breeder reactors, dismantled isotope capability, phasing out US fission, and bureaucracy/ policy/approval hurdles)
  US has key expertise/partners and could enable Heated Air Cycle Engines with Intrinsically Safe approaches (better than jet fuel)
  Requires vision and effort to enable
Chart: Isotope Power versus Half-lIfe
| 700.8 | 700.8 | 24 | 19 | 8 | 59 | 7 | 10 | 9.6999999999999993 | 271 | 242 | 48 | 124 | 3.2 | 271 | 2.8 | 17 | 10512 | 128.6 | 374 | 138 | 160 | 2.65
 | 19.2898 | 86.108 | 27.1428 | 795.7969 | 516.8076 | 14.0065 | 225.5994 | 1472.8438 | 155.9925 | 30.219 | 7.2989 | 309.6187 | 13.8369 | 2606.9204 | 60.7209 | 1548.6195 | 173.1539 | 0.96 | 24.7232 | 50.4281 | 104.1781 | 89.624 | 2303.0428
Enables Hypersonics
Sustainable Ground Power
Enables Conventional Propulsion and Directed Energy
Others actively investing in future propulsion/power capabilities beyond Hydrocarbon Fuels

## Slide 20: Next Steps
Conduct Isotope selection and production scale up study. This would address supply and infrastructure issues.
Develop/validate isotope heat exchanger element performance.
Utilize surrogate, resistance heated heat-exchangers to develop HACE turbine engine. (E.G., inert Thulium 169 electrically heated). Enable ground power, APU, and subsonic propulsion applications.
Develop heat exchanger designs and propulsion systems for high-speed applications. Enable long range and much smaller hypersonic systems.
Heated Air Cycle Engine

## Slide 21: Backup

## Slide 22: Controlling/‘Stopping’ the Engine when you can’t turn the heat off…
Safe Idle
Ground Support (air or water cooled)
Failsafe Heat Exchanger
(Radiant: Heat Loss ~ T4)
Remove or Disperse the Core (separate enough for free convection/radiation)
11
Secondary Loop
Pebble bed – Isotope could be coated and sized so if dispersed, pebbles are small enough to conductively/radiatively self-cool.

## Slide 23: Other Mission Scenarios?
Want a megawatt of electrical power? HACE can do that for an overall system weight of less than 1000 pounds (including fuel) for 4-12 months, eliminating the need for a million gallons of fuel per year.
Need to power an entire base in the middle of nowhere? HACE can make a portable power plant and keep you from having to fly in tankers daily to keep the system refueled.
Need a selectable orbit satellite?
Lightweight/long-range supersonic/hypersonic system with a shorter life heat source?
Avoid refueling OCONUS logistics for cargo/transport aircraft?
Extend the range of LCAAT from thousands of miles to millions of miles?
Launch U2's from a single site?
Have a UCAV/bomber/missileer loiter for months?
Replace a satcom network cheaply/quickly?
Follow/monitor potential threats indefinitely?
Eliminate the need for tanker fighter support?
…
Eliminate the safety issues associated with a fuel that has 10x the energy density of TNT? (that would be jet fuel)
Enable a propulsion/power cycle that can be adapted to future available heat energy (hybrid, remote-beamed-power, fission, fusion, positrons, ...)?
Heated Air Cycle Engine

## Slide 24: Other Applications
Long-term ISR
Naval Fleet Patrol
Sub Hunting
Sub Herding
Long Range Torpedo
Circling Missile Threat
FOB Power
Directed Energy Power
High-Altitude APU
Heavy Space Climb-out
Global Cruise Missile
Extreme Altitude ISR

## Slide 26: 21 Feb Workshop Suggestions
Utilize NETL Hyper research engine (external heat compatible)
Look at Concentrated solar engines and Nusource (portable nuclear power)
Identify DoE/DoD overlap, communicate interest in dual use tech
Consider CONOPS scenarios/return on investment:
Stealth persistent ISR
Ground Power
Satellite replacement (alterable orbit with orders of magnitude cost reduction)
Energy Resilience (10MW large base system requires ~1M gallons of conventional fuel a month)
Very Long range rapid response (even shorter half-life)
Extended range torpedo/Navy UAV
Prolific Energy enabling capabilities
Etc…
Heated Air Cycle Engine

## Slide 27: NENG 681 Project Results
Tm 170 Selected
Thulium Oxide form highly stable
50% production from Tm169 in 90 days with common US infrastructure
Isotope and Decay Chain Product (Yb in the form of Ytterbium Oxide) stable/compatible to 2200K
Tm169 costs comparable to logistics/costs for 4 months of fuel

## Slide 28: Thulium Fuel Processing
Tm 170 Selected
Thulium Oxide form highly stable
Thulium can be alloyed with reactor-compatible metals such as Zirconia
Able to be pelletized to be charged in power station utilizing 0.001% of the pellet space
HEX made to incorporate standardized pellets
Simplified refueling possible
Notes: Tm best now fueled in commercial power plants due to availability of slow/low-energy neutrons. Looking for isotopes with appropriate high energy neutron cross sections to be fueled on nuke carrier or sub. I think they exist…

## Slide 29: Fuel Processing
Reactors needed to process isotopes
First Energy’s Davis-Besse plant near Toledo Ohio is asking for subsidies since it is no longer competitive with natural gas plants.
First energy threatening to close the plant.
National security argument to be made to help keep nuclear plants open with a secondary purpose.
Processing Tm may be cheap since they are strapped for cash.
Other nuclear plants in a similar situation.
Notes: Tm best now fueled in commercial power plants due to availability of slow/low-energy neutrons. Looking for isotopes with appropriate high energy neutron cross sections to be fueled on nuke carrier or sub. I think they exist…

## Slide 31: Isotopes

## Slide 32: Atomic Transformation Processes
(paper, skin, cell walls)
(aluminum or metal sheet)
(Lead or massive amounts of concrete, earth, …)
(water, concrete)
Alpha (Helium)
Beta – (electron)
Beta + (positron)
Gamma
Neutron
Shielding
Notes: In the human body, Potassium 40 (naturally occurring) 4400 decays per second produce 4000 natural positrons per day (511 keV gamma rays).
Potassium-40 is a rare example of an isotope that undergoes both types of beta decay. About 89.28% of the time, it decays to calcium-40 (40Ca) with emission of a beta particle (β−, an electron) with a maximum energy of 1.33 MeV and an antineutrino. About 10.72% of the time it decays to argon-40 (40Ar) by electron capture, with the emission of a 1.460 MeV gamma ray[1] and a neutrino. The radioactive decay of this particular isotope explains the large abundance of argon (nearly 1%) in the earth's atmosphere, as well as its abundance compared to 36Ar. Very rarely (0.001% of the time) it will decay to 40Ar by emitting a positron (β+) and a neutrino.

## Slide 33: Potassium Decay
Banana Equivilant In the human body, Potassium 40 (naturally occurring) 4400 decays per second produce 4000 natural positrons per day (511 keV gamma rays).
~89% B-
~11% Electron Capture with 1.46 MeV gamma ray
0.001% B+ with positron (which annialtes to produce 511 keV gamma rays)
Notes: Potassium-40 is a rare example of an isotope that undergoes both types of beta decay. About 89.28% of the time, it decays to calcium-40 (40Ca) with emission of a beta particle (β−, an electron) with a maximum energy of 1.33 MeV and an antineutrino. About 10.72% of the time it decays to argon-40 (40Ar) by electron capture, with the emission of a 1.460 MeV gamma ray[1] and a neutrino. The radioactive decay of this particular isotope explains the large abundance of argon (nearly 1%) in the earth's atmosphere, as well as its abundance compared to 36Ar. Very rarely (0.001% of the time) it will decay to 40Ar by emitting a positron (β+) and a neutrino.

## Slide 34: Alpha Decay
Alpha particles have a typical kinetic energy of 5 MeV (or ≈ 0.13% of their total energy, 110 TJ/kg) and have a speed of about 15,000,000 m/s, or 5% of the speed of light. There is surprisingly small variation around this energy, due to the heavy dependence of the half-life of this process on the energy produced (see equations in the Geiger–Nuttall law). Because of their relatively large mass, +2 electric charge and relatively low velocity, alpha particles are very likely to interact with other atoms and lose their energy, and their forward motion can be stopped by a few centimeters of air. Approximately 99% of the helium produced on Earth is the result of the alpha decay of underground deposits of minerals containing uranium or thorium.
Example: Uranium 238 to Helium and Thulium 234 (which eventually decays to Lead 206)

## Slide 35: Beta Decay
B- Electron emission
Neutron loses electon, converts to Proton
B+ Positron emission
Proton loses positron, converts to Neutron
  Positron will annilate as soon as it hits an electron, typically producing a gamma ray

## Slide 36: Electron Capture
Nucleus ‘captures’ an electron, converting a Proton into a Neutron.
Higher level electron then replaces missing electron (typically with emission)

## Slide 37: Gamma Decay
Excited nucleus achieves more relaxed state with high energy photon emission: Gamma rays are typically higher energy than x-rays, and penetrate and ionize.

## Slide 38: Air Force Prize Make more reliable, efficient engines using jet fuel
“Bending the cost curve” - SAF
In 1903, the Wright Brothers developed a new, light-weight engine to power their glider…
Today, the Air Force seeks a highly efficient turbine engine to sustain the systems of tomorrow…

## Slide 39: State of the Art Propulsion Cycle Efficiencies Thermal Efficiency versus Pressure Ratio
Chart: 
Mil Turboshafts
Civ Turboshafts
Chart: OPR
| 1.4 | 1.5999999999999999 | 1.7999999999999998 | 1.9999999999999998 | 2.1999999999999997 | 2.4 | 2.6 | 2.8000000000000003 | 3.2 | 3.6 | 4 | 4.4000000000000004 | 4.8000000000000007 | 5.2000000000000011 | 5.6000000000000014 | 6.0000000000000018 | 6.5000000000000018 | 7.0000000000000018 | 7.5000000000000018 | 8.0000000000000018 | 9.0000000000000018 | 10.000000000000002 | 12 | 14 | 16 | 18 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 70 | 80 | 90 | 100
0.90 Comp/Turb, 2200F Conv Turb | 0.046304 | 0.071694 | 0.093395 | 0.11213 | 0.12868 | 0.1433 | 0.15649 | 0.16839 | 0.18914 | 0.20677 | 0.22195 | 0.23535 | 0.24703 | 0.25741 | 0.26689 | 0.27548 | 0.28508 | 0.29372 | 0.3016 | 0.30853 | 0.32103 | 0.33153 | 0.34835 | 0.36104 | 0.37097 | 0.37881 | 0.38537 | 0.39631 | 0.40218 | 0.40493 | 0.40531 | 0.40359 | 0.40038 | 0.39588 | 0.39024 | 0.37537 | 0.35682 | 0.33405 | 0.30791
50hp, w/ SOA Scaling | 0.051858 | 0.079775 | 0.10297 | 0.12256 | 0.13929 | 0.15373 | 0.16628 | 0.17725 | 0.19539 | 0.20955 | 0.22067 | 0.22941 | 0.23624 | 0.24152 | 0.24553 | 0.24848 | 0.25092 | 0.25224 | 0.25263 | 0.25226 | 0.24975 | 0.24551 | 0.23385 | 0.22002 | 0.20545 | 0.19091 | 0.17683 | 0.14474 | 0.11755
SI (Otto) | 0.3 | 0.36
CI (Diesel) | 0.42 | 0.46
~Atkinson (Compound) | 0.47 | 0.375
Brayton (Conv Turbine) | 0.36585 | 0.38462 | 0.42 | 0.12
OPR: Overall Pressure Ratio or Compression Ratio is a measure of technical complexity, cost, and weight
Notes: OPR or Pressure Ratio is indicative of technical sophistication, complexity, structural weight, investment, etc…
Black line is ideal gas turbine with stated compressor/turbine efficiencies and T41 limit.
Higher pressure ratio is better to a point, then increased compression work starts to hurt.
Data points are Current and SOTA real engines.
SI (Otto cycle): Rotax (160hp) and Multipulse DI Research Engine (100hp, 300lb)
DI (Diesel): Thielert (125hp) and SOTA VW TDI (90hp)
Brayton:
Jetcat: 52 lb thrust, 5 lb)
AE2100/T406 (CV-22, C-130J): 6000hp, 971 lb
RR Trent 60 DLE: 70,000hp, 13100 lb
Compound (Atkinson like)
Wright R-3350: 3400hp, 2670lb
Napier Nomad: 3155hp, 3580lb
Surface Ship: 8. Wartsila-Sulzer RTA96-C * Engine Type: Two-cycle, 14-cylinder, inline * Displacement: 1,556,002 ci (25,480L) Yikes! * Bore and Stroke: 38x98 in (Roughly a 3 foot bore and 8 foot stroke!) * Aspiration: Turbocharged * Governed Speed: 102 rpm * Engine Weight: 2,300 tons (The city block-sized crank weights 300 tons) * Dimensions: 89 feet long and 44 feet high * Maximum Power: 108,920 hp at 102 rpm * Maximum Torque: 5,608,312 lb-ft at 102 rpm * Efficiency: 1,660 gallons per hour of heavy fuel oil

## Slide 40: Energy Storage
Energy Source Energy density
HC (typ, + 15 parts air) ~4.3 x 10E7 J/kg
Metals (Al, Boron, etc. + air) ~2-6 x 10E7
H2 (+ 30 parts air) ~12 x 10E7
Methane (CH4) ~5 x 10E7
Explosives ~5 x 10E6
Fuel Cell ~1-5 x 10E6
Battery ~1-3 x 10E5
Spring ~1 x 10E3
Flywheel ~.2-3 x 10E6
Pressure (LN2) ~3 x 10E5
Pressure (3000psi air) ~.4-1 x 10E5
Hydraulic Accumulator ~1 x 10E5
RadioIsotope x 10E10 to 10E12
Fission (U235) ~8.2 x 10E13
25MW portable Fission x 10E2 per second (on semi trailer)
Fusion (D+T) ~5.6 x 10E14
Antimatter (p+e) ~9.0 x 10E16
Notes: Portable Fission, 4x10e5 per hour, 2 days ~ 16 MJ/kg (HC at 30% eff), 259 MJ/kg per month, 3x10e9 per year, 3x10e10 per decade…

## Slide 41: Sustainable Air Power
F-16
Fuel: 600gph (20MW) at best cruise
Endurance: hours
Ops Tempo: 20-60 hrs/month
Strike Capability: lots
Combined ACC flight hours
(F-15, F-16, F-22, F-35, U-2):
96,000 hrs Annually
126,500,000 gallons
(1300 gphr avg)
MQ-1b
Fuel: 4gph (130kW) at best cruise
Endurance: 24 hours
Ops Tempo: 300 hrs/month
Strike Capability: 2
360,000 hrs
1,500,000 gallons
(4 gphr)
Formerly the Cheapest Combat Air Patrol
Cheaper Combat Air Patrol
Notes: Numbers cited are from peak of Iraq/Afghanistan Gulf War

## Slide 42: MQ-1b Case Study
Takeoff/Climbout 100kW
Cruise on 40kW
Internal Combustion Engine:
200 lbs
~30% efficient
1080 hr rated life (4 engines/year!)
50 hr maintenance cycles
360 hr overhaul cycle (1/month!!)
250 hr MTBF (> 1/month!!!)
Fuel: 10 gph takeoff/climbout for 1 hr
4gph cruise for 24hrs
Total Fuel ~600 lb
Propulsion and Fuel
~800 lb

## Slide 43: Predator Airframe Hits 20,000 hrs
80,000 gallons of fuel
$1.3M in gas at shipping terminal
plus delivery to point-of-issue
Over 500 takeoffs/landings
Over 30 engines
60 engine overhauls
($5M+)
Probably 100 turbochargers
($1.5M+)
Probably 50 ‘engine failures’
Notes: Numbers cited are from peak of Iraq/Afghanistan Gulf War

## Slide 45: Conventional Turbine
Compressor
(squeezes air)
Turbine (power extraction to drive compressor)
Shaft (transmits power)
Bearing
Nozzle (thrust) or
Power Turbine (power generation)
Combustor
(converts chemical energy to heat)
Jet Fuel (~42 MJ/kg)
Air
(cycle working fluid)
Fuel Injector
Case
Modest Efficiency (10-40% depending upon scale/throttle)
Cycle Waste Heat leaves as exhaust (thrust)
Inherently Reliable (no sliding seals)

## Slide 46: Turbine Cycle Energy Input
Combustor
(only used for takeoff/climb/dash)
RadioIsotope Heat Exchanger
(sized for cruise power)
Combustor
Conventional Turbine
Heated Air Cycle
Turbine (HACT)
Throttleable
Waste Heat leaves as exhaust
Refuel for 4-13 months
Minimize takeoff/landings/fuel logistics
Select:
low energy decay isotope to mitigate shielding requiriments
‘Short’ half-life that are benign in years
Significantly higher efficiency and power density than conventional RTG/TEG
Design for intrinsic safety
Throttleable
Waste Heat leaves as exhaust
Fly for hours/days

## Slide 47
Radioactive Nuclide Production for Radioisotope Propulsion
Air Force Institute of Technology
14 December, 2017
Notes: Capt Leslie

## Slide 48: Overview
NENG 681 Looked at Po 210 and Tm 170
Po 210 from Bi 210:
  low production potential
  Low melting temperature
  Product is Lead (low melting temperature)
Tm 170 from Tm 169
  High production potential
  Product is Yb 170 (stable)
Notes: Capt Leslie
diffusivity

## Slide 49: Bi-209 Irradiation
Isotope | Po-210 | Bi-209 | Bi-210 | Tl-206 | Bi-210m | Pb-206
Grams | 2.01E-05 | 0.999 | 1.06E-06 | 1.44E-08 | 1.65E-05 | 1.39E-05
Ci | 9.02E-02 | ~0 | 1.31E-01 | 9.68E-04 | ~0 | 2.01E-05
Watts | 3.02E-04 | ~0 | 0.000302 | 3.10E-06 | ~0 | 0
Low production of Po-210 in volume.
Result expected from low absorption cross section of Bi-209.
Nearly all Bi-209 remains after 8 months of irradiation.
Low contribution isotopes not included (~0)
Total 0.0032 W/g-feed
Notes: Nick

## Slide 50: Full Irradiation Simulations
Electrical Power Requirements 40 kW
  Assume 30% thermal power efficiency to turbine power
  Iteratively determined requires 164.4 kg of thulium oxide
Radioactive decay requires that the electrical power produced is at End of Life (EOL)
  After EOL, radioisotopes need to be replaced.
  EOL goal of 6 months
Irradiation [90 Days]
Processing and Assembly [2 Months]
Operations [6 Months]
Notes: Nick

## Slide 51: Full Irradiation Simulations
Irradiation Thulium-Oxide for 90 days.
Flux availability:
  Commercial Reactor (Irradiation timescale not great pairing for scheduling with core refuel.
  High Flux Isotope Reactor ~ 10^15 n/cm^2-s flux
US Patent No 3,432,386
Notes: Nick

## Slide 52: Tm-169 Irradiation Mass Production
Starting Mass is 164.4 kg of Thulium Oxide
Large Production of Tm-170, decays to Yb-170
Notes: Nick

## Slide 53: Tm-169 Irradiation Heat Production
Large heat from Tm-172 decays quickly.
  Places restriction on delay time from post-irradiation to operation
Tm-170 has longer half-life, primary source for heat generation.
Notes: Nick

## Slide 54: Material Properties
Banders Nuclear Corporation
Notes: Bryan

## Slide 55: Thermal Properties
No phase changes for the desired temperature ranges, up to 2300 degrees Celsius
From 100/0 Tm/Yb composition to 0/100, the melting temperature was higher than 2300 degrees Celsius
Notes: Bryan

## Slide 56: Thermal Properties
Notes: Bryan

## Slide 57: Thermal Conductivity
[W/m-K]
Notes: Nick

## Slide 58: Heat Profile
Notes: Bryan

## Slide 59: Radiation Properties
Two low energy photons, and Bremsstrahlung effects from two Beta emissions
Notes: Bryan

## Slide 60: Environmental Barrier Coatings (EBC)
Used within aircraft turbine engines to coat the outside of oxidation sensitive components particularly ceramic components which are highly sensitive to oxidation and volatilization
Material requirements:
  High phase stability
  Similar thermal expansion coefficients to the materials they are covering
  Corrosion-resistant
Notes: Amy

## Slide 61: Ytterbium Disilicate EBC
Ytterbium disilicate (Yb2Si2O7) satisfies the characteristics necessary to be used as an EBC
  It can be subjected to up to 1800 K
  High phase stability
  Stress tested for 10,000h with 3% of coating showing signs of degradation
Yb2Si2O7 is a promising option for an EBC to coat the ceramic oxide fuel
Yb2Si2O7 as applied
Heated at 1300°C for 100h
Notes: Amy

## Slide 62: Material Evaluation
Melting Temperatures:
  Tm2O3: 2301 ± 33.5°C
  Yb2O3: 2328 ± 33.5°C
Both remain solid and cubic crystal structure
Yb2Si2O7 coating
Radiation properties:
  Self-shielding
  3 inches of lead maximum
Notes: Amy

## Slide 63: Isotope Selection Questions
  Isotope:
    Production
    Handling
    Decay Chain
    Disposal
    Accident/dispersal
  Mission/Cycle:
    Turbine Cycle
    Isotope Heat Exchanger Requirements
  Heat Exchanger Integration:
    kg per kW
    Temperature Stability (1800-3000 oF with reasonable CTE)
    Packaging (plate-fin/porous/balls/coatings?)
    Heat Exchanger Design

## Slide 64: AFRL/RQTC Advanced Concepts Group
Notes: 6 watt MHD
100 watt combustion
to 650MW

## Slide 65
Solar
17GW from
135,000 TW
Human
~25 TW
50% Fuels
38% Ag/Forestry
Fuels
12 TW
from 630 ZJ
(~1000 years)
Aviation
350 GW
3% of Fuels
1.6% of Human
Global Climate and Energy Project at Stanford (http://gcep.stanford.edu/)
Ver 1.0 April, 2009 © MRS Source: Proceedings of the 2009 MRS Spring Meeting
Global Exergy Flow & Sources
Fusion
3100 ZJ Ore
30,000,000,000 ZJ seawater
Geothermal
20 GW from
15,000,000 ZJ
320,000 TW (crust transfer)
80 TW Volcanic
Fission
300 GW
from 1300 ZJ Ore 360,000 ZJ seawater
Notes: 360 Million km2 x 1000kg/m3 = 360 x10e15 kg of water
Net Solar is 135,000 TW

## Slide 66: Cycle Efficiency with Throttling
Chart: 
| 313.27568760000003 | 300.84397059999998 | 287.7376458 | 274.0563042 | 259.90826499999997 | 244.5446934 | 229.8743796 | 214.8279326 | 201.01260939999997 | 189.2934716 | 178.1499474 | 167.29243959999999 | 156.67738180000001 | 146.2392006 | 135.942834 | 125.7855964 | 115.7192962 | 106.12200620000002 | 97.210812400000009 | 88.445909200000003 | 79.902493399999997 | 71.562064199999995 | 63.459758199999996 | 55.828476600000002 | 48.639722200000001 | 42.022403799999999 | 35.094823999999996 | 28.8972798 | 22.9052586 | 17.356361399999997 | 12.015672799999999
T63 | 0.23066 | 0.22862 | 0.22638 | 0.22398 | 0.22124 | 0.21825 | 0.2149 | 0.21112 | 0.20724 | 0.2035 | 0.1996 | 0.19544 | 0.19106 | 0.18638 | 0.18138 | 0.17602 | 0.17026 | 0.16429 | 0.15833 | 0.15187 | 0.14496 | 0.13756 | 0.12961 | 0.12142 | 0.11266 | 0.10392 | 0.093668 | 0.08313 | 0.071459 | 0.058902 | 0.044725
Shaft Power Output (kW)
Efficiency
T63 Turboshaft

## Slide 67: Fuels…

## Slide 68: Advanced Propulsion Concepts
Alternative Energy Sources