## Slide 1
Effects of Water Entrainment on Shock Propagation from a Nuclear Detonation
MAJ Trenton Freeman
Air Force Institute of Technology
30 January 2020

## Slide 2: Overview
Background and Motivation
Problem
Thesis Objective
Limitations
Theory
Methodology
Results and Analysis
Conclusions
Future Work

## Slide 3: Acknowledgments
Advisor: LtCol Michael Dexter
Committee Members:
  Dr. John McClory
  Maj James Bevins
Applied Research Associates
  Second-Order Hydrodynamic Automatic Mesh Refinement Code (SHAMRC) developers
Research Sponsored by:

## Slide 4: Background and Motivation
Limited Test Ban Treaty, 10 October 1963
  Prevented U.S. ocean, atmospheric, and space nuclear tests
Reliance on Simulations for
  Effects verification
  Functionality
  Threat assessment
  Wartime and mission planning
  Consequence management
Models can take days to develop and execute

## Slide 5: Problem
How much energy is lost from a water surface nuclear detonation
  Quantify through digital image processing of historic nuclear test films
Does Second-Order Hydrodynamic Automatic Mesh Refinement Code (SHAMRC) model energy lost?
Redwood Nuclear Test - June 1958 - Bikini Atoll, Pacific Proving Grounds
Notes:   Water entrainment
  Energy transmission
  Drag

## Slide 6: Thesis Objective
Quantify energy lost in kilotons from a nuclear detonation over water
  Compare results from films of the same detonation taken from different look angles
  Compare results from multiple nuclear detonations
Determine if SHAMRC is accurately modeling shock wave propagation by comparing to film data

## Slide 7: Limitations
Early Fireball Films
  Out of focus causing blurry fireball images
  Zoomed in too closely chopping off fireball in later frames
  Not calibrated properly leading to light saturation (left)
  Cloud Interference (right)
Aspen 319 kT
Tewa 5 MT
Notes: Cameras have a neutral density filter (provides same attenuation at all wavelengths) allowing us to see the decrease in light intensity as shock front cools to tmin. Without the filter the camera would be saturated for the duration of the detonation

## Slide 8: Theory – X-rays
Primary mechanism creating the shock wave
Primary x-rays created from fission fragment coulombic force interactions go on to ionize radiation case and weapon material.
Reradiated x-rays are emitted at lower energy from the ionized weapon case
Streaming x-rays fully ionize air creating
more x-rays as electrons undergo the
bremsstrahlung process
All x-rays produced are absorbed in
tens to hundreds of meters from detonation
Half of the x-ray energy is shared
between thermal and blast at sea level

## Slide 9: Theory - Cube Root Scaling
Compare height and radius of shock to determine apparent yield lost at the surface of the water
Equation 3 represents a cumulative yield lost with n different radii measurements
(1)
(2)
(3)

## Slide 10: Methodology
MATLAB digital image processing
  Determine height and radius
Apply cube root scaling
  Determine apparent yield lost at the water surface
SHAMRC simulation
  412 kT energy pill equivalent to test shot Redwood
  Post process data
  Plot radius and height from simulation with film data

## Slide 11: MATLAB Film Analysis

## Slide 12: Test Shot Aspen 319 kT

## Slide 13
Results and Analysis

## Slide 14: Height & Radius vs Time
SHAMRC began adding small quantities of energy early in the simulation
Total quantity remained under 1% until 18.0148 ms
18 % added from 18.0148 ms to 18.1079 ms
Simulation results to 18 ms used for analysis

## Slide 15: SHAMRC 18ms & Redwood Frame 45

## Slide 16: SHAMRC 412 kT 1.0 ms

## Slide 17: SHAMRC 412 kT 18.0 ms

## Slide 18: Films
Test | Yield [kT] | Film Number | Station | Distance to GZ [m]
Redwood | 412 | 52533 | 1514.03 | 15216.39
Fir | 1360 | 50992 | 1510 | 37166.14
Fir | 1360 | 50999 | 1514.04 | 18924.38
Aspen | 319 | 52328 | 1510 | 37200.06
Aspen | 319 | 52334 | 1514.04 | 18937.60
Aspen | 319 | 52343 | 1514.03 | 29888.98
Maple | 213 | 52184 | 1514.03 | 15210.10
Maple | 213 | 52185 | 1514.03 | 15207.95
Maple | 213 | 52191 | 1514.04 | 23493.22

## Slide 19: Aspen 319 kT
Error Bars
  2 percent film shrinkage in the upper bound error bar only
  Quantification of error in sensitivity parameter of image processing code

## Slide 20: Aspen 319 kT

## Slide 21: Conclusions
Apparent yield lost from 9 films examined ranged from 10 to 22 percent
Distinct difference in height and radius in all images during the times of interest
Weapons effects are dampened along the surface of water due to water entrainment, energy transmission and drag effects
Evaluate impacts to nuclear targeting, threat assessments, and consequence management

## Slide 22: Future Work
Leverage simulations from other high-fidelity multi-physics codes such as ALE3D and MIRANDA
Analyze additional films for more data points to draw more concrete conclusions
Compare detonations over water to detonations over land
Conduct shock tube experiments to determine if the loss terms of water entrainment, energy transmission into the water, and drag effects can be decoupled

## Slide 23: Questions

## Slide 24
Backup Slides

## Slide 25: Limitations
Shock front identification as detonation approaches tmin
  Shock wave becomes increasingly opaque as it cools preventing the transmission of light from the diffusively growing inner fireball
  Neutral density filter restricts too much light from reaching camera lens
SHAMRC
  Export controlled – requires Defense Supercomputing Recourse Center’s (DSRC) high performance computing (HPC) environment
  Computationally expensive
  Hierarchy the code itself

## Slide 26: Prompt Energy
2 Types of Fission Energy
  Prompt and Delayed
Prompt Fission Energy
  Fission fragment kinetic energy – comprises 93% of prompt energy and 70% of total weapon yield
  Neutron kinetic energy
  Gamma ray energy
Prompt Fission Energy |  | 
Energy Form | U235 Energy (MeV) | Pu239 Energy (MeV)
Fission Fragment Kinetic Energy | 168 | 172
Neutron Kinetic Energy | 5 | 6
Prompt Gamma Energy | 7 | 7
Total Prompt Energy | 180 | 185

## Slide 27: Hydrodynamic Separation
Hydrodynamic separation occurs in tens of microseconds
The fireball surface growth rate slows to a value less than the shock speed or the speed of sound in the local medium

## Slide 28: Thermal Minimum
Shock wave temperature begins to cool obscuring the diffusively growing inner fireball
Near 3300 K the shock wave becomes fully transparent revealing the surface of the fireball
Assume the shock wave is the fireball surface even after hydrodynamic separation to allow the “shock wave” surface to be identified on films
Observed
Breakaway
~3000C
Second
Thermal Maximum
~8000C
Hydrodynamic
Separation
Notes: Cameras have a neutral density filter (provides same attenuation at all wavelengths) allowing us to see the decrease in light intensity as shock front cools to tmin. Without the filter the camera would be saturated for the duration of the detonation

## Slide 29: Camera Types

## Slide 30: Film Selection
Camera issues
  Out of focus causing blurry fireball images
  Zoomed in too closely chopping off fireball in later frames
  Not calibrated properly leading to light saturation (left)
Cloud Interference (right)
Aspen 319 kT
Tewa 5 MT

## Slide 31: Mass of Water Vaporized
Determining the mass of water effected by , the yield loss term
Accounts for drag effects from water, entrainment, and energy transmission into the water
Notes: Q is the heat energy transferred
c is the specific heat 4,186 J/kg*C
L is Latent Heat
No way to decouple effects through these simulations

## Slide 32: Barge Shots
35 Shots Total
13 Shots Y > 1 Mt
2 Shots Y < 10 kt
6 ft < HOB < 15 ft
Available
Analyzed
Notes: Redwood – Film No. 52533
2500 fps
Frames 93 to 210 = 117 frames

## Slide 33: Redwood Film Data Sheet

## Slide 34: Redwood
Yield = 412kT
Film Number 52533

## Slide 35: Redwood
Yield = 412kT
Film Number 52534

## Slide 36
Height & Radius vs Time

## Slide 37: Test Shot Fir 1.36 MT

## Slide 38: Fir 50992

## Slide 39: Fir 50999

## Slide 40: Data Sheet Diameter vs Time

## Slide 41
Height & Radius vs Time
Test Shot Fir: 1.36 MT,

## Slide 42: Radius vs Time

## Slide 43: Uncertainty Analysis
Additional 2.5% on upper bound error bar only to compensate for 2.5% film shrinkage as quantified by LLNL

## Slide 44: Uncertainty Analysis

## Slide 45: Redwood Sensitivity Analysis Frame 20

## Slide 46: Redwood Sensitivity Analysis Frame 70

## Slide 47: Redwood Sensitivity Analysis Frame 130

## Slide 48: SHAMRC 412kT

## Slide 49: 1.0 ms

## Slide 50: 2.0 ms

## Slide 51: 3.0 ms

## Slide 52: 4.0 ms

## Slide 53: 14.0 ms

## Slide 54: 18.0 ms

## Slide 55: 18.0 ms