## Slide 1
Using an Astrophysical Model to Characterize Nuclear Dust
2LT Anita Dunsmore
6 February 2018
Thesis Defense

## Slide 2: Dust Cloud Characterization
Sponsor: Defense Threat Reduction Agency (DTRA)
Advisor: Dr. John McClory
Committee:
  LtCol Brian J. Fry
  LtCol James R. Fee

## Slide 3: Outline
Introduction
Theory
Methodology
  Building the Input Files
Results
  Initial
  Altered Values
  Observed Data
Analysis
  Lessons Learned

## Slide 4: Motivation
Don’t currently have a full picture of the dust cloud after an explosion
Needed for planning and consequence management
  Aircraft
  Communications
  Nearby cities
Must understand all effects of a weapon to plan for the use effectively

## Slide 5: Research Goals
Can models from astrophysics be used for nuclear dust clouds?
  Choose an astrophysical model to try
  Determine if there are any intrinsic barriers to using it for a nuclear dust cloud
  Compare the results to observations to determine accuracy

## Slide 6: Historical Background
Mostly concentrated on fallout
  DEFLIC, HPAC, etc.
  Care about how fallout particles are dispersed long-term
  Less about short-term modeling
Very little about early cloud modeling – chemically and physically complex
  Only simplistic models used (e.g. the distribution of large particles is based on a “power law” – power unknown)
  Mostly older models – less computational power

## Slide 7: Theory
Proposed solution: use a model from astrophysics of a supernova
  Very studied area
Core-collapse supernova: fusion until Fe core, collapse past a certain limit causes the explosion
Similarities
  General physical situation: compression, explosion
  Effects: shock waves, radiation fields, dust clouds
Differences
  Scope of explosion (density, time, distance, etc.)
Will the differences be minimal enough for the solution to still work?

## Slide 8: Overview of Options
Chemical analysis
  Equations describing processes that would change the chemical composition
  Stoichiometric equations, radioactive decay, etc.
  Chose a finite number of elements/compounds to follow
    Equations depended on the specific properties of the element/compound
Usability for nuclear dust clouds
  Equations would have to change based on materials in nuclear explosion
    Would not really be using the astrophysical model

## Slide 9: MOCASSIN: Introduction
Monte Carlo SimulationS of Ionized Nebulae
  Used MC approach to model radiative transfer through dust and gas clouds
3 dimensional (asymmetry – ground burst)
Stochastic
Solves thermal balance and ionization equilibrium equations in grid – iterates until values converge
  Difference between iterations small

## Slide 10: MOCASSIN: Setup
Input files
  Describe entire physical situation
    Source – temperature, power, radius, output spectrum
    Dust and gas – densities, distribution, composition
  Give parameters of the trial
    Convergence criteria
    Number of photons
    Number of iterations
    Wavelength range of output

## Slide 11: MOCASSIN: Algorithm
Tracks photons through gas/dust cloud
Groups them in “energy packets” of specific frequencies
  Computationally efficient
  Originally determined by the flux of the source, emitted isotropically in random directions
Packets tracked through cells
  Either pass through, scatter, or absorb
    Scatter: frequency unchanged, direction changed
    Absorbed: both changed
    Overall energy stays the same
  Tracked until the edge of the grid – recorded
Check convergence criteria after finished – iterate if needed
  Gas only or both: rate of change of neutral hydrogen
  Dust only: rate of change of dust temperatures

## Slide 12: MOCASSIN: End Result
Sum of photons from code – spectral output (SED)
  Wavelength dependent
  Asymmetric – can depend on the direction of output
Wavelength range
  Infrared for dust “shining”
    Optical photons absorbed and re-emitted at longer wavelengths
Compare output to observed
  Change input values for closest match possible

## Slide 13: Problem Space
Dust starts to form at 2000-3000 K – choose 2500
  Gas in MOCASSIN is ionized - want as early as possible
  Need inner fireball source to still be present
Phase of fireball at 2500 K: hydrodynamic growth
  After breakaway – inner fireball and transparent shock wave
  Mixing has not yet occurred – only materials from air, weapon
Type of bomb
  Doesn’t matter – model with input files

## Slide 14: Methodology
Build approximate input files representing several nuclear explosions
  Run files to see if any issues occur
  Approximate – need answers before beginning, so all will be guesses (just need OOM)
Input files to create:
  Main – describes source, run parameters
  Density – describes distribution of dust/gas
  Dust/gas abundance – relative amounts of compounds/elements
    Dust – optical constants of dust compounds
    Gas – abundances of ionized elements

## Slide 15: Explosion Parameters
Need to pick explosions – yield, HOB, bomb design
Operation Dominic Harlem
  1.1-1.2 MT, 4160 m (note: will use 1 MT for input values)
  Only data found
Fat Man
  20 kT, 550 m
  Published bomb design

## Slide 16: General Input Values
All based on fireball temperature of 2500 K
  Assume constant in fireball
Assume scalability
  Time
  Fireball radius (use breakaway)

## Slide 17: Dust and Gas by Zone
Not yet distinguishing between – need to know sources
3 zones:
  Inside fireball: weapon debris, ionized air
    Ionized air out to hydrodynamic separation
  Between fireball and shock: air based on Sedov-Taylor
  Outside shock: ambient air

## Slide 18: Weapon Debris
20 kT – Fat Man
  Used known design, assumed evenly distributed throughout fireball
1 MT – Dominic Harlem
  W-47Y2 Polaris warhead with a Mk-36 casing
  Mostly steel
  Bomb: largely depleted U
  Scaled Fat Man for explosives, etc. to get correct mass

## Slide 19: Air
Assumed 1% molar fraction of water, 78% , 21%
Sedov-Taylor code (LtCol Fry)
  Self-similar
  Solves equations using dimensionless quantities
Assumptions in code
  Diatomic gas (
  Uniform density atmosphere
  3 dimensions

## Slide 20: Dust vs. Gas
Need: dust compounds, elements of gas
Very oxygen-rich
Rules of formation:
  Form as much as possible (astrophysics)
  Form metal oxides
    and – don’t matter which (chose and )
    (suboxides - gas)
    and – plot
  Rest is in gaseous form (N, H, O)

## Slide 21: Final Hydrogen Density
All H in gaseous form
Density used for gas abundances (density file)
3 zones for calculation
  Even split for mesh
Would not have “hard” edges – product of using zones

## Slide 22: Radius Distribution
Later fireball dust cloud – log-normal, with a mean dependent on the explosion type (larger near the ground)
Our fireball – earlier -> smaller dust particles
Mean of air burst: 0.1 micron
Use of mean for ours

## Slide 23: Dust Optical Files
List of and values for different wavelengths
Temperature dependent – need at 2500 K
  Easy to find at wrong temperature
  Calculating temperature dependence is very complex
Used room temperature for all
Constants:
  Sublimation temperature, density, average mass of atom in compound
  Neutral grain potential – photoelectric yield per absorbed photon
    Calculated using metal work function (probably not accurate because metal work functions are very sensitive to precise conditions)

## Slide 24: Results
While running: output files update at each iteration
  Percent converged and “no hit cells”
    No hit cell – cells where no photon interactions occurred
  Current SED output
Stop when:
  Reach 100% convergence
  Reach number of iterations in input file
  Manually stopped

## Slide 25: Results
Output expectations: blackbody with discrepancies from dust/gas absorption and emission
Evaluating outputs
  Cases where something didn’t work – evaluated based on other outputs, not by looking into the code for answers
Convergence/no hit cell combinations
  100% convergence, 0% no hit cells: ideal
  0% convergence, 100% no hit cells: photons all escaped with no interaction
  0% convergence, <100% no hit cells: photons did not escape
    SED with all 0 values

## Slide 26: Initial Tests
Regular input files: no final output
  1 MT: 3% convergence, 95% no hit cells, 8 iterations, 1418 hours
  20 kT: 0% convergence, 84% no hit cells, 1 iteration, 611 hours
  SED outputs all 0 (no photons escaped)
  Stopped due to convergence levels not changing
Want to discover why tests didn’t work – run tests with altered values to see what works and what doesn’t
  Changing densities, radii, temperature
  Run with dust, gas, and both

## Slide 27: Gas Only
2 possibilities
  Finish set number of iterations within 1 minute, 0 % convergence, 100% no hit cells
  Stop after 1 iteration with 0% convergence, 100% no hit
Changes due to input variable alterations indistinguishable from changes due to stochastic nature
No hit cells + SED output = no photon interactions

## Slide 28: Increased Temperature
Recall: MOCASSIN assumes gas to be ionized
  Computes amount in each ionization level
Percent in neutral state for runs with gas
  usually 100%, always over 94% (for gas-only and initial tests)
Need to increase ionization levels – gas is not being properly modeled if it is not ionized
Increase temperature for initial tests to 15,000 K
Results mostly unchanged (SED 0, around 0-4% convergence)
  Ionization level changes:
    C: 100% -> 99.45%
    N: 100% -> 99.0%
    O: 100% -> 99.6%
Not realistic to increase more - earlier time

## Slide 29: Reduced Outer Radius
Air attenuates IR wavelengths a lot
Try at different radii (where the observer would be)
  Right outside shock wave
  Right outside fireball
  Inside fireball
All SEDs were 0
Over 90% no hit cells, 0% convergence
  density of fireball is too large
Cannot work with densities in this range

## Slide 30: Dust Only
Gas-only unsuccessful – try to run with only dust to see if gas is the main problem
Regular parameters
Very similar to initial results
  SED of 0
  Both kept iterating, but convergence not increasing
    Note: stopping after 1 iteration only occurred when gas was present
  20 kT: 5% convergence, 94% no hit
  1 MT: 3% convergence, 96% no hit
  No hit cells + SED of 0 = density too high
Problems with both gas and dust

## Slide 31: Reduced Density
Reduce by 2 OOM until results obtained
1 MT: Density reduced by 2 OOM (in all 3 zones)
  Successful trials (100% convergence, non-zero spectra)

## Slide 32: Repeated Trials
Ensure trials yield same results

## Slide 33: Density Comparisons
For dust and gas – can reduced density give features?
Flattening and wavelength changes

## Slide 34: Alternate Air Modeling
Problems with trials so far:
  Not enough ionization -> need higher temp -> earlier time
  Density values too large -> need later time
Ideal: model the situation at a later time with lower densities
Need to model the gas without requiring ionization
Model gas as a dust with optical constants
Did not work
  Allocation error?
  Error in our input files?
  Radial distribution file

## Slide 35: Observed Data

## Slide 36: Conclusions
Early problems: Optical files
  Need exact numbers
    Temperature dependence
    Work functions
  Everything else is approximate and going to be changed
Problems during tests
  Ionization of gas
    Temperature increase did not help
  Density values
    Lower density has different features
  Modeling air as gas
    Unsuccessful for various reasons
Conclusion: MOCASSIN is not a viable option for modeling a nuclear dust cloud.

## Slide 37: Lessons Learned
Chose MOCASSIN because it would not need to be remade for a nuclear fireball
  Ended up being too inflexible
Need a model that can be adapted, but not entirely redone
  Changed for higher densities
  Different form of elements – ionization
  Distances, times, etc.

## Slide 38: Questions

## Slide 39: Backup Slides
Calculations from Methodology
All values from Methodology
Time – use previous figure, scale for 1 MT
Power
  ,

## Slide 40: Nuclear Input Values

## Slide 41: Fat Man Weapon Debris

## Slide 42: 1 MT Weapon Debris

## Slide 43: Air Composition

## Slide 44: Elements in Fireball

## Slide 45: Oxygen Used

## Slide 46: Dust Molecules

## Slide 47: Gaseous Elements

## Slide 48: Main Input File

## Slide 49: Abundance Files
1 MT Abundance
20 kT Abundance
Air

## Slide 50: Optical File Constants

## Slide 51: Optical Constants
Optical Constants
Optical Constants

## Slide 52: Dominic Harlem Data
Example Data Page

## Slide 53: Filled Data Set
Filled Data in cal/um/sec

## Slide 54: 20 kT Tests

## Slide 55: 1 MT Tests